## Slide 1: Distance Machine Locker
iOS Dev Scout (25 Apr 2017)
SP Digital Tech Talk (12 Jan 2017)
By: Yeo Kheng Meng (yeokm1@gmail.com)
and Vina Rianti (https://github.com/vinamelody)
https://github.com/yeokm1/distance-machine-locker

## Slide 2: Problem?
Red Team
+ unlocked machines

## Slide 3: Trail of destruction

## Slide 4: Solution?
Distance-measuring system
Locks machine when I leave

## Slide 5: Demo

## Slide 6: System overview
Distance Sensor
Arduino Uno
Swift Desktop app

## Slide 7: Agenda
Hardware Device
Swift App
Defensive strategies
Vina’s contribution

## Slide 8: Hardware

## Slide 9: Active IR distance sensor
Active Infrared (IR) Distance Sensor
Effective range: 10 to 80cm
Source: http://education.rec.ri.cmu.edu/content/electronics/boe/ir_sensor/1.html

## Slide 10: Alternative sensor 1: Passive IR
Range 7m
Can only detect presence
Higher error rate

## Slide 11: Alternative sensor 2: Ultrasonic
2cm to 4m
“Noisy” results

## Slide 12: Putting them all together
Arduino Uno in casing meant for Mega 2560
Mounting-hole compatible
Arduino Uno
Arduino Mega 2560

## Slide 13: Arduino firmware
Arduino IDE
Prints cm distance via USB Serial Port

## Slide 14: Host App
Swift 3 Menubar app
Receives Data from USB-Serial Port
Locks machine on threshold reached
Distance (cm) via
USB-Serial

## Slide 15: About the Menubar app
Menubar app (MainMenu.xib, MenuController.swift)
  No Main Window, dock icon
  No Storyboards, just a single xib

## Slide 16: About the app: Serial Port Communication
Uses SwiftSerial library written by yours truly
https://github.com/yeokm1/SwiftSerial
https://engineers.sg/v/1275

## Slide 17: About the app: Locking
Lock screen (Locking.swift)
Use IOKit (suggested by http://stackoverflow.com/a/16368803 )
CGSession –suspend hides notification
  /System/Library/CoreServices/Menu Extras/User.menu/Contents/Resources/CGSession –suspend

## Slide 18: Potential Hacking and Defensive Strategies?

## Slide 19: Hack 1: Disconnecting device
Defence:
  Lock machine immediately
  Issue system notification
  Detect device disconnect: USBWatcher.swift hooks to IOKit
  http://stackoverflow.com/a/41279799
Auto-reconnection when device is plugged back

## Slide 20: Hack 2: Tamper hardware to provide incorrect values
Defence: Vigilant monitoring of distance values on menu bar

## Slide 21: Hack 3: Reprogramming with malicious firmware
Defence: Reprogram Arduino before using it
  Mac App contains hex (firmware) file exported from Arduino IDE
  Flashes hex file with avrdude within Arduino.app
Mac App
Arduino.app
avrdude
firmware.hex

## Slide 22: A possible “undetectable” hacking strategy
Overwrite the Arduino bootloader

## Slide 23: Typical Arduino Programming
Arduino IDE
USB cable

## Slide 24: Microcontroller programming the actual way
Using dedicated programmers with ICSP port
ICSP – In-circuit system programmer
Image sources:
http://www.atmel.com/tools/atatmel-ice.aspx
http://blog.alrightythen.de/2014/08/debugging-with-the-new-atmel-ice/
+
=

## Slide 25: What is an Arduino bootloader?
Allows Arduino IDE to program Arduino board via USB

## Slide 26: Vina Rianti

## Slide 27: Key learnings
Experience turns into idea (or request) on how to make it better
  Distance options too long (10 to 80)
  Don’t lock my machine immediately

## Slide 28
How to shorten the Locking Distance?
Make the option every 5 cm instead of 1 cm
for distance in DISTANCE_MINIMUM...DISTANCE_MAXIMUM {
let distanceMenuItem = NSMenuItem(title: String(distance), action: #selector(distanceMenuItemClicked), keyEquivalent: "")
distanceMenuItem.target = self
if distance == currentLockingDistance{
distanceMenuItem.state = NSOnState
}
distanceMenu.addItem(distanceMenuItem)
}
var option = 5
let DISTANCE_MINIMUM = 10
let DISTANCE_MAXIMUM = 80
for i in DISTANCE_MINIMUM...DISTANCE_MAXIMUM {
if option >= DISTANCE_MAXIMUM {
break
} else {
option += 5
}
print(option)
}
Notes: Give Swift normal for loop example

## Slide 29
for distance in stride(from: DISTANCE_MINIMUM, through: DISTANCE_MAXIMUM, by: 5) {
let distanceMenuItem = NSMenuItem(title: String(distance), action: #selector(distanceMenuItemClicked), keyEquivalent: "")
distanceMenuItem.target = self
if distance == currentLockingDistance{
distanceMenuItem.state = NSOnState
}
distanceMenu.addItem(distanceMenuItem)
}
How to shorten the Locking Distance?
Can I do it more elegantly?
Notes: Give Swift normal for loop example

## Slide 30
How to prevent immediate locking?
Add a Locking Delay: 0, 1, 3, 5 seconds
Out of distance
Time
T1
Example: 3 seconds delay
Not going to lock
Within distance
Current time – T1 > 3 seconds ? Lock !
Time
Out of distance
T1
Question: How does the code work?

## Slide 31
Show me the code!
func distanceReceived(distance: Int){
...
if lockingMode && distance >= currentLockingDistance {
if goingToLock == false {
goingToLock = true
startLockingWindow(start: true)
} else {
startLockingWindow(start: false)
}
} else {
goingToLock = false
}
}
func startLockingWindow(start: Bool) {
if start {
launchLockWindow = CFAbsoluteTimeGetCurrent()
} else {
let elapsed = CFAbsoluteTimeGetCurrent() - launchLockWindow
if elapsed >= Double(lockingTimeout) {
locking.lockMachine()
}
}
}

## Slide 32: Hackers always win
No physical security -> No security
Any Questions?
https://github.com/yeokm1/distance-machine-locker