## Slide 1: Distance Machine Locker
iOS Dev Scout (25 Apr 2017)
SP Digital Tech Talk (12 Jan 2017)
By: Yeo Kheng Meng (yeokm1@gmail.com)
and Vina Rianti (https://github.com/vinamelody)
https://github.com/yeokm1/distance-machine-locker

## Slide 2: Problem?
Red Team
+ unlocked machines

## Slide 3: Trail of destruction

## Slide 4: Solution?
Distance-measuring system
Locks machine when I leave

## Slide 5: Demo

## Slide 6: System setup overview
Distance Sensor
Arduino Uno
OLED screen
(Debugging)
Mac Menubar app

## Slide 7: Agenda
Hardware Device
Swift App
Defensive strategies
Vina’s contribution

## Slide 8: Hardware

## Slide 9: Active IR distance sensor
Infrared (IR) Distance Sensor GP2Y0A21YKR
Effective range: 10 to 80cm
Active IR
Source: http://education.rec.ri.cmu.edu/content/electronics/boe/ir_sensor/1.html

## Slide 10: Alternative sensors?
Passive IR
  7m
  120° cone
  High false positives
Ultrasonic
  2cm to 4m
  Lack precision
  Noisy

## Slide 11: Putting them all together
Arduino Uno in case meant for Mega 2560
Arduino Uno
Arduino Mega 2560

## Slide 12: Arduino firmware
Arduino IDE
Sharp IR library
  https://github.com/guillaume-rico/SharpIR
Prints cm distance via USB Serial Port

## Slide 13: Host App
Swift 3 Menubar app
Receives Data from USB-Serial Port
Locks machine on threshold reached

## Slide 14: About the app
Uses SwiftSerial library written by yours truly
  https://github.com/yeokm1/SwiftSerial
Menubar app (MainMenu.xib, MenuController.swift)
  No Main Window
  No Storyboards, just a single xib
Lock screen (Locking.swift)
  Use IOKit (suggested by http://stackoverflow.com/questions/1976520/lock-screen-by-api-in-mac-os-x )
  CGSession –suspend hides notification
    /System/Library/CoreServices/Menu Extras/User.menu/Contents/Resources/CGSession -suspend

## Slide 15: Potential Hacking Strategies and Defenses

## Slide 16: Hack 1: Disconnecting device
Defense:
  Lock machine immediately
  Issue system notification
  Detect device disconnect: USBWatcher.swift
  http://stackoverflow.com/a/41279799
Auto-reconnection
Need to delay between locking and showing notification (2 seconds)
  MenuController.swift

## Slide 17: Hack 2: Tamper hardware to provide incorrect values
Defense: Vigilant monitoring of distance values on menu bar

## Slide 18: Hack 3: Reprogramming with malicious firmware
Defense: Reprogram Arduino before using it
Swift App contains hex (firmware) file exported from Arduino IDE
Flashes hex file with avrdude to Arduino before using
DistanceSensor.swift and UtilityFunctions.swift

## Slide 19: A possible “undetectable” hacking strategy
Overwrite the Arduino bootloader

## Slide 20: Typical Arduino Programming
Arduino IDE
USB cable

## Slide 21: Microcontroller programming the actual way
Using dedicated programmers with ICSP port
ICSP – In-circuit system programmer
Image sources:
http://www.atmel.com/tools/atatmel-ice.aspx
http://blog.alrightythen.de/2014/08/debugging-with-the-new-atmel-ice/
+
=

## Slide 22: What is an Arduino bootloader?
Allows Arduino IDE to program Arduino board via USB
On reset, wait 1 second for computer to program board before resuming

## Slide 23: Vina Rianti

## Slide 24: Key learnings
Experience turns into idea (or request) on how to make it better
  Too fast to get locked
  Distance options too long
Look at the code … it’s a Mac App!
  Learn to understand how it works
What I learned?
  Git fork and public repo flow
  Not the usual way of coding in Swift ..
    Stride
    CFAbsoluteTime

## Slide 25
for distance in DISTANCE_MINIMUM...DISTANCE_MAXIMUM {
for distance in stride(from: DISTANCE_MINIMUM, through: DISTANCE_MAXIMUM, by: 5) {
let distanceMenuItem = NSMenuItem(title: String(distance), action: #selector(distanceMenuItemClicked), keyEquivalent: "")
distanceMenuItem.target = self
if distance == currentLockingDistance{
distanceMenuItem.state = NSOnState
}
distanceMenu.addItem(distanceMenuItem)
}
Locking Distance option for every 5 cm
Before
After

## Slide 26
Locking Delay
func distanceReceived(distance: Int){
...
if lockingMode && distance >= currentLockingDistance {
if goingToLock == false {
goingToLock = true
startLockingWindow(start: true)
} else {
startLockingWindow(start: false)
}
} else {
goingToLock = false
}
}
func startLockingWindow(start: Bool) {
if start {
launchLockWindow = CFAbsoluteTimeGetCurrent()
} else {
let elapsed = CFAbsoluteTimeGetCurrent() - launchLockWindow
if elapsed >= Double(lockingTimeout) {
locking.lockMachine()
}
}
}

## Slide 27: Hackers always win
No physical security -> No security
Questions?
https://github.com/yeokm1/distance-machine-locker